## Slide 1: Electrical Power Subsystem
SeungGwon Jeon, SeongYeop Yoo
Geuk-Nam Kim

## Slide 2: Contents
Overview
Requirements & Constraints
Components & Interface
Electrical Power Budget
Energy Balance Analysis
Verification Plan
Conclusion

## Slide 3: Overview

## Slide 4: Introduction
 | Electrical Power Subsystem (EPS)
Objectives | Manage power supply and distribution to subsystem components, and generate electrical power
Contents | EPS requirements and constraints EPS components: power control and distribution, battery, solar panel Electrical power interfaces: power supply, power generation, power storage Power analysis: budget, energy balancing Verification and validation: test plan (component  integrated EPS)

## Slide 5: EPS Architecture
Hierarchy
EPS
Electrical Power
Subsystem
SA
Solar Array
Level 4
Level 5
PCDU
Power Conditioning
& Distribution Unit
BAT
Battery
Solar Cell
Bypass Diode
Temp. Sensor
Micro Processor
Unit
Power Conditioning
Module
Power Distribution
Module
Battery Charge
Regulator
Activation Switch
Temp. Sensor
Micro Processor
Unit
Li-ion 18650 Cell
Heater
Activation Switch
Temp. Sensor
<EPS hierarchy diagram>

## Slide 6: Requirements & Constraints

## Slide 7: Subsystem Requirement [1/2]
Level 4
LEVEL 4 | Electrical Power Subsystem (EPS) Requirements |  |  |  | Verification Method |  |  |  | C/N
ID | Title | Requirements | Rationale | Contents | A | I | T | D | 
EPS-001 | Deactivation before Separation | 위성의 궤도진입 이전 EPS가 활성화 되어 있으면 안됨 | SYS-026 | 데이터시트 RBF/Kill Switch 인터페이스 확인 |  | O |  |  | C
EPS-002 | Electrical Power Distribution | 정격 전압 3.3 V, 5.0 V, 12.0 V, 비정격 전압을 각 서브시스템에 공급해야 함 | SYS-026 | 데이터시트를 통한 전원 인터페이스 확인 |  | O |  |  | C
EPS-003 | Component Lifetime | EPS 구성요소는 6개월 이상 안정적으로 동작해야 함 | SYS-001 | 데이터시트 확인 |  | O |  |  | C
EPS-004 | Minimum Electrical Power Generation | EPS 구성요소는 임무 종료 시 까지 평균 5.4 W (TBD) 이상의 전력 생산이 가능해야 함 | SYS-026 | 전력 버짓 분석 | O |  |  |  | C
EPS-005 | Maximum Electrical Power Load | EPS 구성요소는 임무 종료 시 까지 최대 순간전력 15 W (TBD)를 공급 가능해야 함 | SYS-026 | 전력 버짓 분석 | O |  |  |  | C
EPS-006 | Electrical Power Margin | Normal Mode에 대해 전력시스템 Margin은 최소 40% (TBD) 이상 유지해야 함 | SYS-026 | 전력 버짓 분석 | O |  |  |  | C

## Slide 8: Subsystem Requirement [2/2]
Level 4
LEVEL 4 | Electrical Power Subsystem (EPS) Requirements |  |  |  | Verification Method |  |  |  | C/N
ID | Title | Requirements | Rationale | Contents | A | I | T | D | 
EPS-007 | Thermal Condition | EPS 구성요소는 준비 기간동안 보관 온도 및 임무 기간동안 작동 온도범위를 유지해야 함 | SYS-022 | 데이터시트 확인 |  | O |  |  | C
EPS-008 | Harness Dimension | Harness는 허용전류 및 전압 강하를 고려하여, 구조체와 간섭 없는 굵기의 전선을 사용해야 함 | SYS-020 | 데이터시트 확인 및 두께 측정 |  | O |  |  | C
EPS-009 | Health Status Monitoring | 전압, 전류, 온도 등 보드 상태 정보를 자체적으로 수집할 수 있어야 함 | SYS-012 | 데이터시트 확인 |  | O |  |  | C
EPS-010 | Fault Management | 전자부품의 고장을 검출 및 수집이 가능해야 함 | SYS-013 | 데이터시트 확인 |  | O |  |  | C
EPS-011 | Electrical Power Control | 각 서브시스템을 On/Off 시킬 수 있는 스위치 기능을 가지고 있어야 함 | SYS-013 | 데이터시트 확인 |  | O |  |  | C
EPS-012 | Systems Ground | 전체 위성 시스템에 최소 1점 이상의 접지 영역을 제공해야 함 | SYS-026 | 데이터시트 확인 |  | O |  |  | C

## Slide 9: Component Requirement [1/3]
Level 5
LEVEL 5 | Power Control & Distribution Unit (PCDU) Requirements |  |  |  | Verification Method |  |  |  | C/N
ID | Title | Requirements | Rationale | Contents | A | I | T | D | 
PCDU-001 | Maximum Input Power Condition from Solar Array | 태양전지판으로 부터 받는 전압의 크기는 BCR 채널 별 2.0 A와 16.0 V를 넘지 않아야 함 | EPS-003 | 인터페이스를 고려한 생산 전력 분석을 통해 채널별 입력 전압/ 전류 확인 | O |  |  |  | C
PCDU-002 | Thermal Condition | PCDU는 -50~+65℃ 사이에서 보관되어야 하며, -40~+85℃ 사이에서 정상 작동 가능해야 함 | EPS-007 | 데이터시트 확인 |  | O |  |  | C
PCDU-003 | Minimum Input Power Condition from Battery | 배터리로부터 받는 전압의 크기는 12.4 V 이상이 되어야 함 | EPS-006 | 에너지균형 분석을 통해 방전깊이 및 최소 배터리 전압 확인 | O |  |  |  | C
PCDU-004 | Electrical Power Charging Method | 배터리를 충전하기 위한 Power Regulation 기법으로는 MPPT (Maximum Power Point Tracker)를 지원해야 함 | EPS-004 | 데이터시트 확인 |  | O |  |  | C
PCDU-005 | Output Bus Voltage Channel | 각 서브시스템에 전력을 공급하는 각 BUS는 3.3 V, 5.0 V, 12.0 V, 비정격 전압으로 정해져 있어야 함 | EPS-002 | 데이터시트 확인 |  | O |  |  | C
PCDU-006 | Output Switchable Voltage Channel | 각 서브시스템 3.3 V, 5.0 V, 12.0 V, 비정격 전압에 대해 전력공급 및 스위칭이 가능해야 함 | EPS-011 | 데이터시트 확인 후 OBC 연동시험 |  | O |  |  | C

## Slide 10: Component Requirement [2/3]
Level 5
LEVEL 5 | Solar Array (SA) Requirements |  |  |  | Verification Method |  |  |  | C/N
ID | Title | Requirements | Rationale | Contents | A | I | T | D | 
SA-001 | Thermal Condition | 태양전지판은 -40~+85℃ 사이에서 정상 작동 가능해야 함 | EPS-007 | 데이터시트 확인 | O |  |  |  | C
SA-002 | Protection from Inverse Current | 태양전지판은 자체적으로 역전류를 방지하는 회로를 구성해야함 | EPS-003 | 데이터시트 확인 |  | O |  |  | C
SA-003 | Solar Array Interface | 태양전지판의 생산 전압 및 전류가 EPS 구성요소 내 BCR 회로의 허용치 이내가 되도록 셀 연결이 구성되어야 함 | EPM-001 | 인터페이스를 고려한 생산 전력 분석을 통해 채널별 입력 전압/ 전류 확인 | O |  |  |  | C
SA-004 | Health Status Monitoring | 태양전지판은 전압과 전류가 모니터링 되어야 함 | EPS-009 | 데이터시트 기반 수신 가능 상태 정보 종류 및 형식 확인 |  | O |  |  | C

## Slide 11: Component Requirement [3/3]
Level 5
LEVEL 5 | Battery (BAT) Requirements |  |  |  | Verification Method |  |  |  | C/N
ID | Title | Requirements | Rationale | Contents | A | I | T | D | 
BAT-001 | Maximum Battery DOD | Normal Mode에서 DoD가 20% 이하, 임무 기간동안 DoD 40% 이하이어야 함 | EPS-006 | 에너지균형 분석을 통해 방전깊이 확인 | O |  |  |  | C
BAT-002 | Thermal Condition | 배터리는 보관 시 -20~+20℃ 사이를 유지해야 하며, 충전 시 +0~+45℃, 방전 시 -20~+60℃ 사이에서 정상 작동 가능해야 함 | EPS-007 | 데이터시트 확인 |  | O |  |  | C
BAT-003 | Charge & Discharge | 배터리 충전-방전 횟수는 5000회 이상 되어야 함 | EPS-003 | 데이터시트 확인 |  | O |  |  | C
BAT-004 | Battery Capacity | 배터리 용량은 24 Wh (TBD) 이상이어야 함 | EPS-006 | 데이터시트 확인 |  | O |  |  | C
BAT-005 | Battery Temperature | 배터리 셀의 온도는 항상 5℃ 이상으로 유지되어야 함 | EPS-007 | Heater 작동을 고려한 열해석 결과 분석 후 우주 환경 시험 수행 |  |  |  | O | N
BAT-006 | Health Status Monitoring | 배터리의 전압과 온도가 모니터링 되어야 함 | EPS-009 | 데이터시트 기반 수신 가능 상태 정보 종류 및 형식 확인 후 OBC 연동시험 |  |  | O |  | N

## Slide 12: EPS Specification
Contents | Requirements and Constraints | Specifications
Power Generation | > 5.4 W (40% margin, normal mode) | > 10.57 W (67.6% margin, normal mode)
Solar Input | 3.5~16.0 V (each channel) < 2 A (each channel) | < 13.5 V (+X-axis) < 1.0 A (+Y-axis)
Depth of Discharge | < 20% (mission lifetime) | < 13.20% (mission mode)
Capacity | > 24 Wh (mission lifetime) | 45 Wh
Electrical Load | < 2 A (each channel) < 4 A (total current draws) | < 1.88 A (5 V bus, communication mode) < 3.88 A (communication mode)
Thermal Control | 0~+45℃ (battery cell) | +10~+35℃ (heater on battery pack)
<EPS main specifications>

## Slide 13: Components & Interface

## Slide 14: EPS Components [1/4]
ISIS Modular EPS Type C: Integrated PCDU and Battery
  Configuration: 16 V & 45 Wh battery (4S-1P, Panasonic NCR 18650B)
<Configuration of ISIS modular EPS type C>
Integrated PCDU & Battery (Type C)
PCDU
Battery Pack
Configuration | Description | Note
Output | Regulated: 3.3 V (4 ch.), 5 V (3 ch.), 12 V (1 ch.) Battery bus: 12.4~16.0 V (3 ch.) | All switchable
Input | 3.5~16.0 V & < 2 A | Each channel, MPPT
Protection | Under-/over-voltage cut-off & watchdog timer | -
Power Dissipation | Typ. 90 mW | Battery heater < 2.5 W
Conversion Efficiency | Typ. 90% | Depend on loads
Li-ion Battery Cell

## Slide 15: EPS Components [2/4]
Solar Array Configurations
  TJ Solar Cell 3G30C (Azur Space): optimized for LEO missions at EOL
  Configuration: single deployable panel & body-mounted panel
    Mechanical constraint: 3U & total extrusion < 7 mm
    Electrical constraint: maximum generation per channel, 3.5~16.0 V / < 2.0 A
    Self-deployment mechanism: thermal knife to cut wire
    Telemetry: coarse sun sensor (photo-diode) / temperature sensor
PX-BSP (4S-1P): 10.8 V & 0.5 A
MX-BSP (5S-1P): 13.5 V & 0.5 A
Y-DSP (3S-2P): 8.1 V & 1.0 A
<Configuration of solar array>

## Slide 16: EPS Components [3/4]
Deployment Circuit
  Input power
      5 V PDM  < 0.4 A/circuit
  Logic
      PWR on  MOSFET EN  Deploy  Detect (3V3 GPIO)  MOSFET DIS  PWR off
      Detect switch: Panasonic, AV404461
      Mosfet switch: Infelon, BTS711L1
<Configuration of circuit for solar array deployment>

## Slide 17: EPS Components [4/4]
Wire
  Hook-up wire (Belden)
    Low- outgassing, internal resistance, heat resistance
    AWG24~16 (Teflon coated)
Board-to-board Connector
  PicoLock (Molex)  most EPS components
    Extremely low height + (relatively) high current rate
  DF13 (Hirose)  vertical type
    Easy to fabricate and connect
  Micro D (Glenair)  only star tracker
Credit: Belden
<AWG24/26 hook-up wire>
Credit: Molex
Credit: Hirose
Credit: Glenair
<Board-to-board connectors>
Notes: TML < 1.0 , CVCM < 0.1 for aerospace application /

## Slide 18: EPS Interface
Electrical Power Interface
<EPS interface diagram>
CNDH
ADCS
OBC
FSS
CSS
GPS
RX
RWA
STT
MTQ
3.3 V
3.3 V
5.0 V
3.3 V
VBATT
5.0 V
PWM
PAY
CAM
BBB
3.3 V
5.0 V
12.0 V
-X-axis
5S-1P
+X-axis
4S-1P
-Z-axis
2S-1P
-Y-axis
3S-2P
+Y-axis
3S-2P
SA
MPPT4
MPPT3
MPPT0
MPPT1
MPPT2
PCDU
13.5 V / 0.5 A
10.8 V / 0.5 A
5.4 V / 0.5 A
8.1 V / 1.0 A
8.1 V / 1.0 A
BAT
4.2 V
Li-ion
Cell
4.2 V
Li-ion
Cell
4.2 V
Li-ion
Cell
4.2 V
Li-ion
Cell
4S-1P (16.8 V)
Separation SW
Separation SW
RBF SW
SW
Daughter
Board
Mother Board
COMS
UHF
TRX
STX
5.0 V
3.3 V
5.0 V

## Slide 19: Electrical Power Budget

## Slide 20: Overview
Power Generation & Consumption
    Required electrical power margin > 40%
    Desired depth of discharge < 20%
    Conversion efficiency > 90%
    Electrical configurations of solar array and battery
    Orbital parameter & coefficient for orientations  power generation
    Average power draws considering duty rate of components
<Overview of power budget calculator>
Normal & Peak Power Draw (W)
Average
Power Draw (W)
Parameter Setting
Analysis Results

## Slide 21: Power Generation
Mean Power Generation Analysis by LTAN & Orientation
  To meet power requirements, normally orient to the Sun
  Reference orbit with 700 km altitude & LTAN16 for system design & analysis
<Mean power generation by LTAN & orientation>
10.57 W
5.15 W
LTAN 16
Orientation | Mean Power Generation (W)
Sun-pointing | 10.49~16.32
Nadir-pointing | 2.00~5.67

## Slide 22: System Operations
Components Duty Rate by Scenarios
Contents |  | Normal Mode |  | Mission Mode |  | Communication Mode |  | Charge Mode | 
Component | Sub- system | Daylight | Eclipse | Daylight | Eclipse | Daylight | Eclipse | Daylight | Eclipse
CAM | Payload | off | off | 300 sec | off | off | off | off | off
BBB | Payload | off | off | 600 sec | off | off | off | off | off
OBC | CNDH | always | always | always | always | always | always | always | always
Temp. Sensor | CNDH | always | always | always | always | always | always | always | always
IMU/MMT | ADCS | always | always | always | always | always | always | always | always
FSS/CSS | ADCS | always | always | always | always | always | always | always | always
GPS RX | ADCS | always | always | always | always | always | always | always | always
STT | ADCS | off | off | 1000 sec | off | (1000 sec) | (1000 sec) | off | off
MTQ | ADCS | 5 sec on (20% mag.) : 5 sec off | 5 sec on (20% mag.) : 5 sec off | 5 sec on (40% mag.) : 5 sec off | 5 sec on (40% mag.) : 5 sec off | 5 sec on (40% mag.) : 5 sec off | 5 sec on (40% mag.) : 5 sec off | 5 sec on (20% mag.) : 5 sec off | 5 sec on (20% mag.) : 5 sec off
RWA | ADCS | 1 sec Torque : 9 sec Speed | 1 sec Torque : 9 sec Speed | 2 sec Torque : 8 sec Speed | 1 sec Torque : 9 sec Speed | (2 sec Torque : 8 sec Speed) | (2 sec Torque : 8 sec Speed) | 1 sec Torque : 9 sec Speed | 1 sec Torque : 9 sec Speed
UHF TRX | COMS | 1 sec Tx : 30 sec Rx | 1 sec Tx : 30 sec Rx | 1 sec Tx : 30 sec Rx | 1 sec Tx : 30 sec Rx | 1 sec Tx (300 sec Tx) : 30 sec Rx | 1 sec Tx (300 sec Tx) : 30 sec Rx | 1 sec Tx : 30 sec Rx | 1 sec Tx : 30 sec Rx
S-band TX | COMS | off | off | off | off | off (600 sec Tx) | off (600 sec Tx) | off | off
PCDU | EPS | always | always | always | always | always | always | always | always
Battery | EPS | always (w/o heater) | always (w/o heater) | always (w/o heater) | always (w/o heater) | always (w/o heater) | always (w/o heater) | always (w/o heater) | always (w/o heater)
<Summary of components duty rate by scenarios>

## Slide 23: Electrical Power Margin
Summary of Results
  Electrical power margin > 41.42% at communication mode (> 40% always)
  Required battery capacity > 18.63 Wh (with depth of discharge 20%)
  Max. channel load < 1.88 A (< 2.0 A per each channel)
Operational Modes |  | Detumbling* | Normal | Mission | Communication | Charge
Power Consumption (W) | Total Average | 1.16 | 3.43 | 5.08 | 5.56 | 2.34
Peak Load (A) | 3.3 V (Mother) | 1.09 | 1.50 | 1.50 | 1.50 | 1.17
 | 5 V (Mother) | 0.41 | 0.41 | 0.63 | 1.88 | 0.41
 | 5 V (Daughter) | 0.00 | 0.00 | 0.51 | 0.00 | 0.00
 | 12 V (Daughter) | 0.00 | 0.00 | 0.47 | 0.00 | 0.00
 | VBATT (Mother) | 0.01 | 0.51 | 0.51 | 0.51 | 0.51
 | Total Battery | 1.51 | 2.42 | 3.62 | 3.89 | 2.09
Power Generation (W) | Orbit Average | 2.53 | 10.57 | 9.49 | 9.49 | 10.57
Power Margin Value (W) |  | 1.37 | 7.14 | 4.41 | 3.93 | 8.23
Power Margin (%) |  | 54.27 | 67.59 | 46.49 | 41.42 | 77.82
Battery Capacity (Wh) |  | 3.88 | 12.37 | 18.33 | 18.63 | 7.86
Battery Capacity (Ah) |  | 0.27 | 0.86 | 1.27 | 1.29 | 0.55
<Summary of electrical power budget results>
* Detumbling Case: MTQ duty rate = 15% & OBC/FSS/CSS/Temp. Sensor/Beacon On

## Slide 24: Energy Balance Analysis

## Slide 25: Overview
Energy Balance Analysis
  Current dynamics modeling
    Li-ion battery model (ISIS battery pack, 14.4 V & 45 Wh)
    PV cell array model (Triple Junction AZUR solar cell, 30% efficiency)
  Battery SoC affected by power generation and consumption
    Balanced SoC over orbital period
    Minimized DoD over mission lifetime
    MPPT efficiency affected by body spins (Erb et al., 2011)
      BCR with constant current charging method (fractional open circuit voltage/current)
    PCM output efficiency by electrical load
<Energy balance analysis flow diagram>
<Configuration of EPS components>
Integrated PCDU & Battery (Type C)
PCDU
Battery
Solar Array

## Slide 26: Mathematical Model [1/6]
Generic Battery Dynamic Model  “Non-linearity”
  Charge current
  Discharge current
  Perturbations
    Temperature effect, aging effect, …
: extracted capacity (Ah)
: low frequency current dynamics (A)
: battery current (A)
: polarization resistance (Ω)
: constant voltage (V)
: exponential voltage (V)
: exponential capacity (Ah-1)
<Dynamic Li-ion battery model for system simulation (Mathworks)>
Notes: MATLAB Simulation Model for Dynamic Mode of the Lithium-ion Batteries to Power the EV (Baboselac, 2017)
A Generic Battery Model for the Dynamic Simulation of Hybrid Electric Vehicle (Tremblay, 2007)
Dynamic Lithium-Ion Battery Model for System Simulation (Gao, 2002)

## Slide 27: Mathematical Model [2/6]
Li-ion Cell: NCR 18650B (Panasonic)
  Nominal voltage: 3.6 V (2.5~4.2 V) & capacity: 3.25~3.35 Ah
  Reference voltage: 0.2-C open circuit voltage (OCV)
  EOC mode (with 1st order low-pass filter): 4.0 V
  Constant internal resistance: 39 mΩ at 25℃ (Wang, 2017)
<Li-ion battery model and general characteristics of NCR 18650B>
Notes: https://kr.mathworks.com/help/physmod/sps/powersys/ref/battery.html
https://kr.mathworks.com/help/sldo/examples/estimate-model-parameters-per-experiment-code.html

## Slide 28: Mathematical Model [3/6]
PV Cell: Azur Space Triple Junction Solar Cell 30% Efficiency
  Current dynamics (Villalva, Gazoli, and Filho, 2009)
<PV cell model with general characteristics>
* : thermal voltage

## Slide 29: Mathematical Model [4/6]
Electrical Load
  Current draw in battery model
    Generated power (W) + “electrical load” (W) = battery charge & discharge rate
    Type
      Continuous (constant); OBC, FSS/CSS, PCDU, RWA speed, …
      Spike (peak); RWA torque, inrush, …
      Pulse (rectangular, trapezoidal, sawtooth, …); MTQ, PPS, …
<Electrical load model and examples>

## Slide 30: Mathematical Model [5/6]
Conversion Efficiency of Regulators
  Solar input to battery
    Allowable input voltage range, 3.5~16.0 V
      Efficiency w.r.t input voltage range, 80~95%
      ** Performance degradations by temperature, body spins & inherent effects
  Battery to switch output
    Output conversion efficiency w.r.t electrical loads of each channel, 70~95%
<Conversion efficiency of regulator by electrical loads (ISIS modular EPS type C)>
Solar Input to Battery
Convertor Chain Efficiency
Battery to Switch Output
Convertor Chain Efficiency
Efficiency
Efficiency
Load Current (A)
Load Current (A)
<Example profiles of solar input with allowable voltage & current values>
Solar Input to Battery: Voltage
Solar Input to Battery: Current
Solar Input to Battery: Triggered Energy

## Slide 31: Mathematical Model [6/6]
Integrated Mathematical Models
  Closed-loop simulation for scenarios
Electrical Load
Power Generation Input
*Orbit/Attitude Dynamics
Battery Model
Conversion Efficiency
Battery Capacity Output
<Integrated mathematical models for energy balance analysis>

## Slide 32: Simulation Results [1/2]
State-of-charge Profiles in Battery Voltage Level
  DOD < 20% & SOC > 50% (initial SOC, 80%) over 1-period
    Considered orbit & attitude dynamics with uncertainties
      Pointing accuracy, 13 deg (3σ)  orientation changes by mission scenarios
    Considered conversion efficiency & cut-off range of solar array input
    H/W component duty rate by mission scenarios
    SOC estimation based on OCV profiles
Mode | Average Power Generation (W) | DOD (%) | End of SOC (%)
Normal | 11.82 | 10.62 | 90.62
Mission | 11.82 | 13.20 | 90.50
Comm. Day | 9.47 | 10.50 | 88.75
Comm. Eclipse | 11.94 | 10.39 | 90.00
Emergency | 11.82 | N/A (30.81) | 80.81
<Summary of energy balance analysis
results by scenarios>
<Example profiles of generated/consumed power &
battery state-of-charge in mission mode>
Orientation Changes
*Initial SOC of Emergency Mode = 50%

## Slide 33: Simulation Results [2/2]
Survivability Analysis in LEOP  “Charging”
  1-day operations & stowed configuration
    Basic operations; (antenna deployment) beacon, detumbling, HK monitoring, …
    Prolonged detumbling periods & (partially) fail to stabilize initial angular velocity
<Summary of energy balance analysis results in LEOP>
Case | Description | Initial ω (deg/sec) | MPPT eff. (%) | Initial SOC (%) | End of SOC (%)
1 | Detumbling Success | 20 (in each axis) | 40~90 | 80 (15.5 V) | 89.93 (15.94 V)
2 | Detumbling Fail (No Control) | 20 (in each axis) | 40 | 50 (14.4 V) | 76.71 (15.29 V)
3 | Detumbling Partially Fail 1 (No Control) | 10 (in each axis) | 60 | 50 (14.4 V) | 89.97 (15.94 V)
4 | Detumbling Partially Fail 2 (No Control) | 5 (in each axis) | 80 | 50 (14.4 V) | 89.96 (15.94 V)
5 | Detumbling Partially Fail 3 (No Control) | 1 (in each axis) | 90 | 50 (14.4 V) | 89.96 (15.94 V)
[Case 2]
[Case 1]

## Slide 34: Verification Plan

## Slide 35: Component Level Testing [1/2]
Integrated EPS Module Type C
  Activation & RBF switch logic; systems shut-down or boot with external switches for each channel
  Check telemetry & telecommand via I2C communication
  Switch functionalities; on-off operations delay, output voltage & current
  Electrical loads using external power supply and electrical load device
    Evaluate conversion efficiency of regulators, line loss, …
<Example configuration of integrated EPS module testing>
Integrated PCDU & Battery (Type C)
EGSE
Test List

## Slide 36: Component Level Testing [2/2]
Solar Array and Sensors
  Measure dark current and evaluate its bypass diode
  Check solar array output measurement with halogen lamp or sunlight
  Check Telemetry & telecommand of sensors; photodiode, temp. sensor, …
Solar Array Deployment Circuit
  Check deployment logic by switch status and power supply
  Check duration of thermal knife operations
<Example configuration of solar array and deployment circuit testing>
Damkjar, 2019

## Slide 37: Integration Level Testing
Integrated EPS Module Type C & Solar Array
  Check telemetry & telecommand via I2C communication
    Repeat component level testing sequences
  Measure solar array output and compare with MPPT input
    Light source using halogen lamp or outdoor sunlight
<Example configuration of integrated EPS module and solar array>
Post, 2013
Measure solar array output as analog values
Light Source
Rotation
0~180 deg
Compare with solar array input on
PCDU’s MPPT port
Notes: https://www.researchgate.net/publication/275460703_A_Low-Cost_Photodiode_Sun_Sensor_for_CubeSat_and_Planetary_Microrover

## Slide 38: Conclusion

## Slide 39: Summary
EPS Configurations & Specifications
  Components; PCDU, Li-ion battery, solar array, deployment circuit, …
  Electrical interface; solar array input & battery output for each channel
  Specifications w.r.t. requirements & constraints  “compliable”
EPS Analysis
  Power budget management
  EPS mathematical model design
  Energy balance analysis; integrated electrical power simulation by scenarios
EPS Verification Plan
  Component level testing plan
  Integration level testing plan

## Slide 40: Issue and Concern
Issue
  From thermal analysis results, battery stack has low temperature margin
    Solution 1) evaluation of thermal analysis results; consultation, STM testing
    Solution 2) insulation using Kapton or MLI/SLI
    Solution 3) change the location of battery in structure model
Concern
  Lack of detailed battery specifications due to none-flight heritage version
    Advanced model based on flight heritage model (since 2018)
    Solution 1) limit DOD during operations within 15% (smaller than recommendation)
    Solution 2) local testing using NCR 18650B li-ion battery cell
  Over current during integration testing
    Solution 1) time-sharing of H/W duty rate and evaluate through ETB testing
    Solution 2) utilize redundant channel for component with high-current draw
  Survival during LEOP
    Solution 1) set on-orbit configurable conditions for detumbling end

## Slide 41: Future Works
Summary of Main Schedule
  Near-term
    Set-up for component level testing environment based on verification plan
    Evaluation of current design through local interface & function testing
      Deployment circuit logic & performance
      Photodiode & temperature sensor bit resolution with amplifier
      Battery cell charge & discharge testing
  Long-term
    EPS component level testing after delivery of COTS
    EPS integration level testing before ETB flat-sat testing
<Example configuration of EPS testing>

## Slide 42: Question & Answer
Thank You for Your Attention

## Slide 43: Appendix.

## Slide 44: Risk Management [1/2]
ID | Detection | Solar Array |  | Battery |  | Solution
 |  | Deployment | Low Power Generation | Heater | Sensors | 
EPS-01 | NO battery telemetry (Battery Temperature) |  |  |  |  | FSW reboot by OBC WDT System reboot by PCDU WDT
EPS-02 | Low battery temperature (Heater Enable Telemetry) |  |  |  |  | Attitude control to heat battery (passive thermal control based on thermal analysis)
EPS-03 | Anomaly in PCDU telemetry (PCDU BCR Voltage, Current) |  |  |  |  | Check a location of damaged solar array Orient to Sun for maximum power generation (tumbling & emergency)
EPS-04 | NO deployment switch signal (Tact Switch GPIO Signal) |  |  |  |  | Check PCDU telemetry Retry to deploy solar array by telecommand (tumbling & emergency)
EPS-05 | NO system responses |  |  |  |  | System reboot by PCDU WDT (generally, it’s a mission failure!)

## Slide 45: Risk Management [2/2]
ID | Detection | PCDU |  |  |  | Solution
 |  | BCR | PDM Switch | WDT | I2C | 
EPS-06 | NO PCDU telemetry (Battery Voltage, Temperature) |  |  |  |  | FSW reboot by OBC WDT System reboot by PCDU WDT
EPS-07 | Fail to contact (Telecommunication failure) |  |  |  |  | Wait system reboot other devices (FSW reboot by OBC command)
EPS-08 | Anomaly in PCDU / component telemetry (PDM Voltage, Current) |  |  |  |  | Compare subsystems telemetry with PCDU PDM telemetry FSW reboot by OBC WDT Disable / Isolate damaged PDM
EPS-09 | Anomaly in BCR telemetry (BCR Voltage, Current) |  |  |  |  | Check PCDU BCR telemetry PCM reboot or system reboot
EPS-10 | NO system responses |  |  |  |  | System reboot by PCDU WDT (generally, it’s a mission failure!)
EPS-11 | NO PDM output or disable to control status |  |  |  |  | Compare subsystems telemetry with PCDU PDM telemetry FSW reboot by OBC command Change system operations
EPS-12 | NO power generation (BCR telemetry) |  |  |  |  | FSW reboot by OBC command (generally, it’s a mission failure!)

## Slide 46: Product Assurance Plan
Scale | Probability of Occurrence | Impact of Occurrence
5 | Almost Certain | Technical goals cannot be reached
4 | Highly Probable | Significant degradation in technical performance
3 | Probable | Moderate reduction of technical performance
2 | Possible | Small reduction in technical performance
1 | Improbable | Minimal or no consequence
5 |  |  |  |  | 
4 |  |  |  |  | 
3 | EPS-04 |  | EPS-05 EPS-06 | EPS-08 | EPS-07 EPS-10
2 | EPS-02 |  | EPS-03 | EPS-09 | EPS-11 EPS-12
1 | EPS-01 |  |  |  | 
 | 1 | 2 | 3 | 4 | 5
Risk
Impact of Occurrence
Probability of Occurrence

## Slide 47: EPS Schedule [1/5]
Main Tasks
6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
EPS Survey
EPS Design
EPS H/W Development
EPS Verification
Month
Year
2021
2019
2020
: Scheduled
: Progress
PDR
CDR

## Slide 48: EPS Schedule [2/5]
Detailed Tasks
6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
EPS Survey
Configuration of EPS
Detailed Function of Components
COTS Selection
Design and Verification Methods
Month
Year
2021
2019
2020
PDR
: Scheduled
: Progress
CDR

## Slide 49: EPS Schedule [3/5]
Detailed Tasks
6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
EPS Design
Requirements and Constraints
Design and Budget Analysis
EPS Internal/ External Interfaces
Energy Balance Simulation
Month
Year
2021
2019
2020
: Scheduled
: Progress
PDR
CDR

## Slide 50: EPS Schedule [4/5]
Detailed Tasks
6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
EPS H/W Development
Solar Panel Deployment Device
Pin-out & Data I/O
Component Performance Testing
Component Functional Testing
Month
Year
2021
2019
2020
: Scheduled
: Progress
PDR
CDR

## Slide 51: EPS Schedule [5/5]
Detailed Tasks
6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
EPS Verification
PCDU/ Battery Flat-sat Testing
PCDU/Solar Array Flat-sat Testing
EPS End-to-end Testing
Month
Year
2021
2019
2020
PDR
: Scheduled
: Progress
CDR

## Slide 52: Wire Diagram [1/4]
Solar Panel: Body-mounted
P1 | Description
1 | Positive
2 | Positive
3 | Negative
4 | Negative
P2 | Description
1 | GND
2 | Temp. Vout
3 | 3V3 SW2
4 | Photodiode
P1 | Description
1 | Positive
2 | Positive
3 | Negative
4 | Negative
P2 | Description
1 | GND
2 | Temp. Vout
3 | 3V3 SW2
4 | Photodiode
Molex Picolock
504050-0491
Molex Picolock
504050-0491
Solar Panel Side Connector
(-X) 5S-1P
Body-mounted
(+Z) 2S-1P
Body-mounted
Mother Board
Daughter Board
MPPT 3
MPPT 4
CSKB
MPPT 0
MPPT 1
MPPT 2
13.5 V & 0.5 A
BRF +X
BRF +Y
5.4 V & 0.5 A
Umbilical External Charging Port
(+X) 4S-1P
Body-mounted
<Solar array to PCDU (mother) wire diagram>
10.8 V & 0.5 A

## Slide 53: Wire Diagram [2/4]
Solar Panel: Deployable [1/2]
BRF +X
BRF +Y
(-Y) 3S-2P
Deployable
(+Y) 3S-2P
Deployable
Mother Board
Daughter Board
MPPT 3
MPPT 4
CSKB
MPPT 0
MPPT 1
MPPT 2
P1 | Description
1 | Positive
2 | Negative
Molex Picolock
504050-0291
Molex Picolock
504050-0291
Solar Panel Side Connector
(+Y) Body-mounted
(-Y) Body-mounted
P1 | Description
1 | Positive
2 | Negative
8.1 V &
1.0 A
P2 | Description
1 | Positive
2 | Positive
3 | Negative
4 | Negative
P2 | Description
1 | Positive
2 | Positive
3 | Negative
4 | Negative
P1 | Description
1 | Positive
2 | Negative
P1 | Description
1 | Positive
2 | Negative
Front
Molex Picolock
504050-0291
Front
Molex Picolock
504050-0291
Via
Via
8.1 V &
1.0 A
<Solar array to PCDU (daughter) wire diagram>
Molex Picolock
504050-0491
Molex Picolock
504050-0491

## Slide 54: Wire Diagram [3/4]
P1 | Description
1 | Positive
2 | Negative
P1 | Description
1 | Positive
2 | Negative
P2 | Description
1 | Positive
2 | Positive
3 | Negative
4 | Negative
Via
Solar Panel: Deployable [2/2]
  Panel to PCDU
Molex Picolock
504050-0291
Molex Picolock
504050-0291
Molex Picolock
504050-0491
<Solar array to PCDU wire diagram>

## Slide 55: Wire Diagram [4/4]
Electrical Interface Board: ADCS
(+X)
Body-mounted
Solar
Panel
4S-1P
Electrical Interface Board (ADCS)
Top View
CSS/Temp SPI0
CSS/Temp Analog
CSS/Temp 3V3
(-X)
Body-mounted
Solar
Panel
5S-1P
(+Y)
Body-mounted
Only
PCB
(-Y)
Body-mounted
Only
PCB
(+Z)
Body-mounted
Solar
Panel
2S-1P
CSS +Z
STT
P4 | Description
4 | GND
3 | Temp. Vout
2 | 3V3 SW2
1 | Photodiode
P5 | Description
- | -
7 | 3V3 SW2
6 | SPI CS1
5 | SPI MOSI
4 | SPI SCK
3 | Photodiode
2 | GND
1 | GND
P3 | Description
4 | GND
3 | Temp. Vout
2 | 3V3 SW2
1 | Photodiode
P2 | Description
4 | GND
3 | Temp. Vout
2 | 3V3 SW2
1 | Photodiode
P1 | Description
4 | GND
3 | Temp. Vout
2 | 3V3 SW2
1 | Photodiode
Molex Picolock
504050-0491
Molex Picolock
504050-0891
On-board Computer
Bottom View
RWL3
RWL2
RWL1
CSS/Temp
RWA/STT
CSS/Temp
RWA/STT
P1 ~ P4
P5
P6 ~ P8
P9
P10 ~ P11
P8 | Description
6 | CAN0 LOW
5 | CAN0 HIGH
4 | GND
3 | 3V3 SW1
2 | 3V3 SW2
1 | VBATT0
P7 | Description
6 | CAN0 LOW
5 | CAN0 HIGH
4 | GND
3 | 3V3 SW1
2 | 3V3 SW2
1 | VBATT0
P6 | Description
6 | CAN0 LOW
5 | CAN0 HIGH
4 | GND
3 | 3V3 SW1
2 | 3V3 SW2
1 | VBATT0
P9 | Description
6 | RS485 A (Rx)
5 | RS485 B (Rx)
4 | RS485 Z (Tx)
3 | RS485 Y (Tx)
2 | GND
1 | 5V SW3
Molex Picolock
504050-0691
Molex Picolock
504050-0691
BRF +X
BRF +Y
<Sensors on solar array to OBC wire diagram>

## Slide 56: Normal Mode
Power Generation
  Sun-pointing: 11.82 W (orbital average)

## Slide 57: Normal Mode
Battery Capacity
  Battery SoC [%] – start at 80%
    DOD = 4.78%
85.26
90.04
4.78

## Slide 58: Normal Mode
Battery Capacity
  Battery voltage [V]
Min 15.56
Max 16.10

## Slide 59: Normal Mode
Power Consumption
  Total output channels

## Slide 60: Normal Mode
Power Consumption
  3.3 V output channels

## Slide 61: Normal Mode
Power Consumption
  5 V output channels

## Slide 62: Normal Mode
Power Consumption
  Battery voltage output channels

## Slide 63: Communication Mode
Power Generation
  Sun-pointing & nadir-pointing: 9.47 W (orbital average)

## Slide 64: Communication Mode (Day)
Battery Capacity
  Battery SoC [%] – start at 80%
    DOD = 11.05%
75.55
86.60
11.05

## Slide 65: Communication Mode (Day)
Battery Capacity
  Battery voltage [V]
Min 15.12
Max 16.15

## Slide 66: Communication Mode (Day)
Power Consumption
  Total output channels

## Slide 67: Communication Mode (Day)
Power Consumption
  3.3 V output channels

## Slide 68: Communication Mode (Day)
Power Consumption
  5 V output channels

## Slide 69: Communication Mode (Day)
Power Consumption
  Battery voltage output channels

## Slide 70: Communication Mode (Eclipse)
Power Generation
  Sun-pointing: 11.82 W (orbital average)

## Slide 71: Communication Mode (Eclipse)
Battery Capacity
  Battery SoC [%] – start at 80%
    DOD = 10.4%
79.6
90
10.4

## Slide 72: Communication Mode (Eclipse)
Battery Capacity
  Battery voltage [V]
Min 15.29
Max 16.16

## Slide 73: Communication Mode (Eclipse)
Power Consumption
  Total output channels

## Slide 74: Communication Mode (Eclipse)
Power Consumption
  3.3 V output channels

## Slide 75: Communication Mode (Eclipse)
Power Consumption
  5 V output channels

## Slide 76: Communication Mode (Eclipse)
Power Consumption
  Battery voltage output channels

## Slide 77: Charge Mode
Power Generation
  Sun-pointing: 11.82 W (orbital average)

## Slide 78: Charge Mode
Battery Capacity
  Battery SoC [%] – start at 80%
    DOD = 3.52%
62.96
66.48
3.52

## Slide 79: Charge Mode
Battery Capacity
  Battery voltage [V]
Min 14.7
Max 15.69

## Slide 80: Charge Mode
Power Consumption
  Total output channels

## Slide 81: Charge Mode
Power Consumption
  3.3 V output channels

## Slide 82: Charge Mode
Power Consumption
  5 V output channels

## Slide 83: Charge Mode
Power Consumption
  Battery voltage output channels

## Slide 84: Mission Mode
Mission mode
  Power generation (Total) 11.82 W

## Slide 85: Mission Mode
Battery Capacity
  Battery SoC [%] – start at 80%
    DOD = 10.45%
80.00
90.45
10.45

## Slide 86: Mission Mode
Battery Capacity
  Battery voltage [V]
Min 15.46
Max 16.12

## Slide 87: Mission Mode
Power Consumption
  Total output channels

## Slide 88: Mission Mode
Power Consumption
  3.3 V output channels

## Slide 89: Mission Mode
Power Consumption
  5 V output channels

## Slide 90: Mission Mode
Power Consumption
  12 V output channels

## Slide 91: Mission Mode
Power Consumption
  Battery voltage output channels

## Slide 92: Power Budget
Component | Product | Operations | Amount | Voltage Input | Current Draw | Current Draw | Power Consumption | Power Consumption | Duty Rate | Duty Rate | Power Consumption
- | - | Nominal | - | - | Nominal | Peak | Nominal | Peak | Nominal | Peak | Average
- | - |  | EA | V | A | A | W | W | % | % | W
CCD Camera | B3420 |  | 1 | 12.0 | 0.425 | 0.425 | 5.10 | 5.10 | 0% | 0% | 0.00
Camera Control Board | BeagleBone Black | Full Load | 1 | 5.0 | 0.210 | 0.460 | 1.05 | 2.30 | 0% | 0% | 0.00
On-board Computer | ARM926EJ-S SAM9X25 | Full Load | 1 | 3.3 | 0.109 | 0.109 | 0.36 | 0.36 | 100% | 0% | 0.36
Temperature Sensor |  | Steady | 5 | 5.0 | 0.160 | 0.000 | 0.000 | 0.00 | 100% | 0% | 0.00
Inertial Measurement Unit | ICM-20689 | Steady | 1 | 3.3 | 0.003 | 0.003 | 0.01 | 0.01 | 100% | 0% | 0.01
Magnetometer | MMC5883MA | Steady | 1 | 3.3 | 0.000 | 0.000 | 0.00 | 0.00 | 100% | 0% | 0.00
Fine Sun Sensor | FSS | Steady | 1 | 3.3 | 0.023 | 0.023 | 0.08 | 0.08 | 100% | 0% | 0.08
Coarse Sun Sensor | CSS | Steady | 5 | 5.0 | 0.000 | 0.000 | 0.00 | 0.00 | 100% | 0% | 0.00
GNSS RX | OEM719A | Steady | 1 | 3.3 | 0.280 | 0.280 | 0.92 | 0.92 | 100% | 0% | 0.92
GNSS Antenna | TW1421 | Steady | 1 | 3.3 | 0.015 | 0.015 | 0.05 | 0.05 | 100% | 0% | 0.05
Star Tracker | KU Leuven Star Tracker | Steady | 1 | 5.0 | 0.200 | 0.200 | 1.00 | 1.00 | 0% | 0% | 0.00
Magnetic Torquer | Air Coil | Full Load | 1 | 5.0 | 0.096 | 0.096 | 0.48 | 0.48 | 0% | 10% | 0.05
 | Rod | Full Load | 2 | 5.0 | 0.134 | 0.134 | 1.34 | 1.34 | 0% | 10% | 0.13
Reaction Wheel | CubeWheel Medium | Steady | 3 | 3.3 | 0.023 | 0.023 | 0.23 | 0.23 | 100% | 0% | 0.23
 |  | Steady (@2000 rpm) | 3 | 14.4 | 0.008 | 0.008 | 0.35 | 0.35 | 90% | 0% | 0.31
 |  | Torque | 3 | 14.4 | 0.144 | 0.144 | 6.21 | 6.21 | 10% | 0% | 0.62
UHF TRX | AX100U | TX (max. RF) | 1 | 3.3 | 0.800 | 0.850 | 2.64 | 2.81 | 0% | 5% | 0.14
 |  | RX | 1 | 3.3 | 0.055 | 0.120 | 0.18 | 0.40 | 95% | 0% | 0.17
UHF Antenna | UHF Antenna III | Steady | 1 | 5.0 | 0.001 | 0.002 | 0.00 | 0.01 | 95% | 5% | 0.00
S-band TX | PULSAR-STX | Idle | 1 | 5.0 | 0.122 | 0.122 | 0.61 | 0.61 | 0% | 0% | 0.00
 |  | TX (max. RF) | 1 | 5.0 | 0.920 | 1.000 | 4.60 | 5.00 | 0% | 0% | 0.00
S-band Antenna | PULSAR-DATA | TX (max. RF) | 1 | 5.0 | 0.000 | 0.000 | 0.00 | 0.00 | 0% | 0% | 0.00
PCDU | ISIS CEPS Type C | Idle | 1 | 14.4 | 0.028 | 0.006 | 0.006 | 0.09 | 100% | 0% | 0.01
Battery | NCR18650B 4S1P | Heater | 1 | 14.4 | 0.156 | 0.156 | 2.25 | 2.25 | 0% | 0% | 0.00
Normal Mode
Power Consumption (W) | Total Average | 3.43 |  | 
Peak Load (A) | 3.3 V (Mother) | 1.50 | < 2 A | per Ch.
 | 5.0 V (Mother) | 0.41 | < 2 A | per Ch.
 | 5.0 V (Daughter) | 0.00 | < 2 A | per Ch.
 | 12.0 V (Daughter) | 0.00 | < 2 A | per Ch.
 | VBATT (Mother) | 0.51 | < 2 A | per Ch.
 | Total Battery | 2.42 | < 4 A | 
Power Generation (W) | Orbit Average (EOL) | 13.34 | Sun-pointing | 
Power Margin Value (W) | Orbit Average | 9.91 |  | 
Power Margin (%) | Orbit Average | 289.38 | > 30% | 
Battery Capacity (Wh) | Orbit Average | 11.49 |  | 
Battery Capacity (Ah) | Orbit Average | 0.80 |  | 

## Slide 93: Power Budget
Mission Mode
Power Consumption (W) | Total Average | 5.56 |  | 
Peak Load (A) | 3.3 V (Mother) | 1.50 | < 2 A | per Ch.
 | 5.0 V (Mother) | 1.88 | < 2 A | per Ch.
 | 5.0 V (Daughter) | 0.00 | < 2 A | per Ch.
 | 12.0 V (Daughter) | 0.00 | < 2 A | per Ch.
 | VBATT (Mother) | 0.51 | < 2 A | per Ch.
 | Total Battery | 3.89 | < 4 A | 
Power Generation (W) | Orbit Average (EOL) | 12.18 | Nadir-pointing | 
Power Margin Value (W) | Orbit Average | 6.62 |  | 
Power Margin (%) | Orbit Average | 119.21 | > 30% | 
Battery Capacity (Wh) | Orbit Average | 18.63 |  | 
Battery Capacity (Ah) | Orbit Average | 1.29 |  | 

## Slide 94: Power Budget
Component | Product | Operations | Amount | Voltage Input | Current Draw | Current Draw | Power Consumption | Power Consumption | Duty Rate | Duty Rate | Power Consumption
- | - | Nominal | - | - | Nominal | Peak | Nominal | Peak | Nominal | Peak | Average
- | - |  | EA | V | A | A | W | W | % | % | W
CCD Camera | B3420 |  | 1 | 12.0 | 0.425 | 0.425 | 5.10 | 5.10 | 0% | 0% | 0.00
Camera Control Board | BeagleBone Black | Full Load | 1 | 5.0 | 0.210 | 0.460 | 1.05 | 2.30 | 0% | 0% | 0.00
On-board Computer | ARM926EJ-S SAM9X25 | Full Load | 1 | 3.3 | 0.109 | 0.109 | 0.36 | 0.36 | 100% | 0% | 0.36
Temperature Sensor |  | Steady | 5 | 5.0 | 0.160 | 0.000 | 0.000 | 0.00 | 100% | 0% | 0.00
Inertial Measurement Unit | ICM-20689 | Steady | 1 | 3.3 | 0.003 | 0.003 | 0.01 | 0.01 | 100% | 0% | 0.01
Magnetometer | MMC5883MA | Steady | 1 | 3.3 | 0.000 | 0.000 | 0.00 | 0.00 | 100% | 0% | 0.00
Fine Sun Sensor | FSS | Steady | 1 | 3.3 | 0.023 | 0.023 | 0.08 | 0.08 | 100% | 0% | 0.08
Coarse Sun Sensor | CSS | Steady | 5 | 5.0 | 0.000 | 0.000 | 0.00 | 0.00 | 100% | 0% | 0.00
GNSS RX | OEM719A | Steady | 1 | 3.3 | 0.280 | 0.280 | 0.92 | 0.92 | 100% | 0% | 0.92
GNSS Antenna | TW1421 | Steady | 1 | 3.3 | 0.015 | 0.015 | 0.05 | 0.05 | 100% | 0% | 0.05
Star Tracker | KU Leuven Star Tracker | Steady | 1 | 5.0 | 0.200 | 0.200 | 1.00 | 1.00 | 10% | 0% | 0.10
Magnetic Torquer | Air Coil | Full Load | 1 | 5.0 | 0.096 | 0.096 | 0.48 | 0.48 | 0% | 20% | 0.10
 | Rod | Full Load | 2 | 5.0 | 0.134 | 0.134 | 1.34 | 1.34 | 0% | 20% | 0.27
Reaction Wheel | CubeWheel Medium | Steady | 3 | 3.3 | 0.023 | 0.023 | 0.23 | 0.23 | 100% | 0% | 0.23
 |  | Steady (@2000 rpm) | 3 | 14.4 | 0.008 | 0.008 | 0.35 | 0.35 | 80% | 0% | 0.28
 |  | Torque | 3 | 14.4 | 0.144 | 0.144 | 6.21 | 6.21 | 20% | 0% | 1.24
UHF TRX | AX100U | TX (max. RF) | 1 | 3.3 | 0.800 | 0.850 | 2.64 | 2.81 | 0% | 5% | 0.14
 |  | RX | 1 | 3.3 | 0.055 | 0.120 | 0.18 | 0.40 | 95% | 0% | 0.17
UHF Antenna | UHF Antenna III | Steady | 1 | 5.0 | 0.001 | 0.002 | 0.00 | 0.01 | 95% | 5% | 0.00
S-band TX | PULSAR-STX | Idle | 1 | 5.0 | 0.122 | 0.122 | 0.61 | 0.61 | 90% | 0% | 0.55
 |  | TX (max. RF) | 1 | 5.0 | 0.920 | 1.000 | 4.60 | 5.00 | 0% | 10% | 0.50
S-band Antenna | PULSAR-DATA | TX (max. RF) | 1 | 5.0 | 0.000 | 0.000 | 0.00 | 0.00 | 0% | 10% | 0.00
PCDU | ISIS CEPS Type C | Idle | 1 | 14.4 | 0.028 | 0.006 | 0.006 | 0.09 | 100% | 0% | 0.01
Battery | NCR18650B 4S1P | Heater | 1 | 14.4 | 0.156 | 0.156 | 2.25 | 2.25 | 0% | 0% | 0.00
Communication Mode
Power Consumption (W) | Total Average | 2.34 |  |  | 
Peak Load (A) | 3.3 V (Mother) | 1.17 | < 2 A | per Ch. | per Ch.
 | 5.0 V (Mother) | 0.41 | < 2 A | per Ch. | per Ch.
 | 5.0 V (Daughter) | 0.00 | < 2 A | per Ch. | per Ch.
 | 12.0 V (Daughter) | 0.00 | < 2 A | per Ch. | per Ch.
 | VBATT (Mother) | 0.51 | < 2 A | per Ch. | per Ch.
 | Total Battery | 2.09 | < 4 A |  | 
Power Generation (W) | Orbit Average (EOL) | 13.34 | Sun-pointing |  | 
Power Margin Value (W) | Orbit Average | 11.00 |  |  | 
Power Margin (%) | Orbit Average | 469.05 | > 30% |  | 
Battery Capacity (Wh) | Orbit Average | 7.86 |  |  | 
Battery Capacity (Ah) | Orbit Average | 0.55 |  |  | 

## Slide 95: Power Budget
Component | Product | Operations | Amount | Voltage Input | Current Draw | Current Draw | Power Consumption | Power Consumption | Duty Rate | Duty Rate | Power Consumption
- | - | Nominal | - | - | Nominal | Peak | Nominal | Peak | Nominal | Peak | Average
- | - |  | EA | V | A | A | W | W | % | % | W
CCD Camera | B3420 |  | 1 | 12.0 | 0.425 | 0.425 | 5.10 | 5.10 | 0% | 0% | 0.00
Camera Control Board | BeagleBone Black | Full Load | 1 | 5.0 | 0.210 | 0.460 | 1.05 | 2.30 | 0% | 0% | 0.00
On-board Computer | ARM926EJ-S SAM9X25 | Full Load | 1 | 3.3 | 0.109 | 0.109 | 0.36 | 0.36 | 100% | 0% | 0.36
Temperature Sensor |  | Steady | 5 | 5.0 | 0.160 | 0.000 | 0.000 | 0.00 | 100% | 0% | 0.00
Inertial Measurement Unit | ICM-20689 | Steady | 1 | 3.3 | 0.003 | 0.003 | 0.01 | 0.01 | 100% | 0% | 0.01
Magnetometer | MMC5883MA | Steady | 1 | 3.3 | 0.000 | 0.000 | 0.00 | 0.00 | 100% | 0% | 0.00
Fine Sun Sensor | FSS | Steady | 1 | 3.3 | 0.023 | 0.023 | 0.08 | 0.08 | 100% | 0% | 0.08
Coarse Sun Sensor | CSS | Steady | 5 | 5.0 | 0.000 | 0.000 | 0.00 | 0.00 | 100% | 0% | 0.00
GNSS RX | OEM719A | Steady | 1 | 3.3 | 0.280 | 0.280 | 0.92 | 0.92 | 0% | 0% | 0.00
GNSS Antenna | TW1421 | Steady | 1 | 3.3 | 0.015 | 0.015 | 0.05 | 0.05 | 0% | 0% | 0.00
Star Tracker | KU Leuven Star Tracker | Steady | 1 | 5.0 | 0.200 | 0.200 | 1.00 | 1.00 | 0% | 0% | 0.00
Magnetic Torquer | Air Coil | Full Load | 1 | 5.0 | 0.096 | 0.096 | 0.48 | 0.48 | 0% | 10% | 0.05
 | Rod | Full Load | 2 | 5.0 | 0.134 | 0.134 | 1.34 | 1.34 | 0% | 10% | 0.13
Reaction Wheel | CubeWheel Medium | Steady | 3 | 3.3 | 0.023 | 0.023 | 0.23 | 0.23 | 100% | 0% | 0.23
 |  | Steady (@2000 rpm) | 3 | 14.4 | 0.008 | 0.008 | 0.35 | 0.35 | 90% | 0% | 0.31
 |  | Torque | 3 | 14.4 | 0.144 | 0.144 | 6.21 | 6.21 | 10% | 0% | 0.62
UHF TRX | AX100U | TX (max. RF) | 1 | 3.3 | 0.800 | 0.850 | 2.64 | 2.81 | 0% | 5% | 0.14
 |  | RX | 1 | 3.3 | 0.055 | 0.120 | 0.18 | 0.40 | 95% | 0% | 0.17
UHF Antenna | UHF Antenna III | Steady | 1 | 5.0 | 0.001 | 0.002 | 0.00 | 0.01 | 95% | 5% | 0.00
S-band TX | PULSAR-STX | Idle | 1 | 5.0 | 0.122 | 0.122 | 0.61 | 0.61 | 0% | 0% | 0.00
 |  | TX (max. RF) | 1 | 5.0 | 0.920 | 1.000 | 4.60 | 5.00 | 0% | 0% | 0.00
S-band Antenna | PULSAR-DATA | TX (max. RF) | 1 | 5.0 | 0.000 | 0.000 | 0.00 | 0.00 | 0% | 0% | 0.00
PCDU | ISIS CEPS Type C | Idle | 1 | 14.4 | 0.028 | 0.006 | 0.006 | 0.09 | 100% | 0% | 0.01
Battery | NCR18650B 4S1P | Heater | 1 | 14.4 | 0.156 | 0.156 | 2.25 | 2.25 | 0% | 0% | 0.00
Charge Mode
Power Consumption (W) | Total Average | 5.08 |  | 
Peak Load (A) | 3.3 V (Mother) | 1.50 | < 2 A | per Ch.
 | 5.0 V (Mother) | 0.63 | < 2 A | per Ch.
 | 5.0 V (Daughter) | 0.51 | < 2 A | per Ch.
 | 12.0 V (Daughter) | 0.47 | < 2 A | per Ch.
 | VBATT (Mother) | 0.51 | < 2 A | per Ch.
 | Total Battery | 3.62 | < 4 A | 
Power Generation (W) | Orbit Average (EOL) | 12.18 | Nadir-pointing | 
Power Margin Value (W) | Orbit Average | 7.10 |  | 
Power Margin (%) | Orbit Average | 139.96 | > 30% | 
Battery Capacity (Wh) | Orbit Average | 17.02 |  | 
Battery Capacity (Ah) | Orbit Average | 1.18 |  |