## Slide 1: Introduction of Electrical Power Subsystem
Geuk-Nam Kim
Room 618 Science Building, 2019.07.11

## Slide 2: Contents
What is EPS?
EPS Configuration
Power Analysis I
Power Analysis II
Conclusion

## Slide 3: What is EPS?

## Slide 4: Overview
Definition
  Manage power supply and distribution to subsystem components, and generate electrical power
Requirement and Constraint
  Activation switch: remove before flight (RBF) / separation switch
  Power interface: voltage regulation and supply / single ground / limitation in capacity / bus or switch voltage supply
  Power generation & consumption (budget): solar panel / duty / margin / depth of discharge / state of charge
  Mechanical design: dimension & mass / battery temperature
  Telemetry & telecommand: health data collection / health data transmission / command reception
  + Etc.: detect and isolate error (watchdog timer, external EDAC) / conformal coating / outgassing …

## Slide 5: EPS Configuration
Hierarchy
EPS
Solar Array
PCDU
Battery
Solar Cell
Bypass
Diode
MCU
PCM
PDM
BCR
Li-polymer
Shield
Activation
Switch
Activation
Switch
Sensors
Deployment
Heater
Sensors
Sensors

## Slide 6: Power Analysis
Budget Management
  Purpose: check EPS capability for the operation of H/W components, and worst case analysis for power consumption and generation
Energy Balance Analysis
  Purpose: check changes of DoD (Depth of Discharge) & SoC (State of Charge) over several periods, and redesign ConOps (Concept of Operations) to satisfy EPS requirements and constraints
  Mathematical system modeling
    Current dynamics: PV cells / battery
    Orbit / attitude dynamics
    Power generation, consumption, charge method, …
  Analysis setting and feasibility-check
    Model validation through H/W test (or numerous case studies)

## Slide 7: EPS Development Scheme
#1. Set Requirements and Constraints
#2. Conceptual Design
  Survey H/W as candidates
  Define electrical power I/O
  Define H/W components-EPS-solar array interface
  Power budget based on ConOps
#3. Software-based Analysis
  Energy balance analysis with mathematical H/W models
#4. Repeat #1~#3
  Until #1 satisfies mission and system requirements
#5. H/W Development: Manufacturing & Verification

## Slide 8: EPS Configuration

## Slide 9: Power Distribution and Control Unit
Main Component to Manage Electrical Power I/O
  BCR: Battery Charge Regulator
    BUCK for high input voltage (~90%) / SEPIC for low input voltage (~80%)
    Internal (or additional) MPPT: Maximum Power Point Tracker
  PCM: Power Conditioning Module
  PDM: Power Distribution Module
Bus Protection
  Over current, battery under voltage
  End of Charge (EoC)
Telemetry & Telecommand
<Clyde Space EPS diagram>

## Slide 10: Solar Panel
Energy Generation
  Solar cells: convert light energy to electrical power through the photovoltaic effect
  Characteristics: low efficiency / sensitive / complicate to assemble / expensive …  But, very light material and highly reliable performance
  Solar array by integrating several solar panels
  Body mount panel / deployable panel
<Solar cell efficiency (1st, NASA credit), commercial CubeSat solar
panel (2nd, Clyde Space), and solar cell attachment (3rd, CANYVAL)>
Notes: https://sst-soa.arc.nasa.gov/03-power

## Slide 11: Battery
Energy Storage
  Type: Li-ion / Li-polymer + Ni-Cd / Ni-MH / Pb / Ni-Zn …
  High energy density to minimize system mass
  Cell balancing technology on multi-string battery
  Inbuilt heater system
  Reliability in a vacuum environment
<Battery efficiency (left, NASA credit) and
commercial CubeSat battery (right, GOMspace and Clyde Space)>

## Slide 12: Others
Deployment
  Deploy UHF antenna or solar array
  Power supply, and need to manage inrush current to protect circuit
Diode and Sensor
  Bypass diode to prevent a backward current
  Photodiode to detect Sun-light (applicable as an attitude sensor)
  Temperature sensor
<Deployable array (left, Pumpkin) and
Antenna deployment (right, M-Cubed)>
<Photodiode on solar panel (CANYVAL-C)>

## Slide 13: Electrical Interface
EPS to Subsystems
  Max. Current / Voltage / Switch
    (Channel) PCM < 4.0 A / PDM < 1.0 A
<EPS function diagram>

## Slide 14: Electrical Interface
Solar Array to EPS
  Input Voltage
    Buck BCR (SA1, SA2): 7.4~30 V  SA2 + SA4/5, SA6/7 (High Power Bundle)
    SEPIC BCR (SA3): 3.0~9.5 V
<Solar array power I/O diagram>

## Slide 15: Power Analysis I: Basic

## Slide 16: Overview: Power Budget
Simple Method for Electrical Power Management
  Calculate the summation of duty cycled H/W power consumptions in each mode operation
  Calculate loads on each bus voltage (limitation on current)
  EPS design criteria: power consumption << generation
  Effective way to manage power consumptions by mode, duty cycled H/W operations, the efficiency of voltage regulation, etc.

## Slide 17: Power Budget [1/4]
Normal Mode: Nadir-pointing
  Beacon: 1 sec transmission by 30 sec / PCM eff. 90%
Subsystem H/W | P Consumption (W) | Duty Cycle (%) | P Operation (W) | Note
Imager | 3.00 | 0 | 0.00 | Multi-spectral
OBC 1 | 2.56 | 0 | 0.00 | SDR / FPGA
OBC 2 | 0.89 | 100 | 0.89 | Main / ADCS
FSS | 0.02 | 100 | 0.02 | -
MTRQ | 1.24 | 25 | 0.31 | 2 X Rod / 1 X Air-coil
RWA | 8.33 | 25 | 2.08 | 3 axis
GPS Rx | 1.11 | 100 | 1.11 | L1
GPS Antenna | 0.11 | 100 | 0.11 | L1
EPS | 0.44 | 100 | 0.44 | PCDU / BCR
Battery | 0.89 | 0 | 0.00 | 40 Wh / Active Heater
UHF TRX | 3.33 | 3 | 0.10 | Beacon / Uplink
UHF Antenna | 0.04 | 100 | 0.04 | Deployable
S-band TRX | 2.11 | 0 | 0.00 | RX Only
S-band Antenna | 13.33 | 0 | 0.00 | Patch
Solar Array 1 | Generate | - | -8.84 | Deployable
Solar Array 2 | Generate | - | -0.50 | Body-mount
Power Margin |  |  | -4.24 | +45.3%

## Slide 18: Power Budget [2/4]
Mission Mode: Nadir-pointing
  Taking images / UHF communication
Subsystem H/W | P Consumption (W) | Duty Cycle (%) | P Operation (W) | Note
Imager | 3.00 | 15 | 0.45 | Multi-spectral
OBC 1 | 2.56 | 30 | 0.77 | SDR / FPGA
OBC 2 | 0.89 | 100 | 0.89 | Main / ADCS
FSS | 0.02 | 100 | 0.02 | -
MTRQ | 1.24 | 50 | 0.62 | 2 X Rod / 1 X Air-coil
RWA | 8.33 | 50 | 4.17 | 3 axis
GPS Rx | 1.11 | 100 | 1.11 | L1
GPS Antenna | 0.11 | 100 | 0.11 | L1
EPS | 0.44 | 100 | 0.44 | PCDU / BCR
Battery | 0.89 | 0 | 0.00 | 40 Wh / Active Heater
UHF TRX | 3.33 | 10 | 0.33 | Beacon / Uplink
UHF Antenna | 0.04 | 100 | 0.04 | Deployable
S-band TRX | 2.11 | 10 | 0.21 | RX Only
S-band Antenna | 13.33 | 0 | 0.00 | Patch
Solar Array 1 | Generate | - | -7.45 | Deployable
Solar Array 2 | Generate | - | -0.43 | Body-mount
Power Margin |  |  | 1.29 | -16.3%

## Slide 19: Power Budget [3/4]
Communication Mode: Nadir-pointing
  S-band & UHF communication
Subsystem H/W | P Consumption (W) | Duty Cycle (%) | P Operation (W) | Note
Imager | 3.00 | 0 | 0.45 | Multi-spectral
OBC 1 | 2.56 | 6 | 0.15 | SDR / FPGA
OBC 2 | 0.89 | 100 | 0.89 | Main / ADCS
FSS | 0.02 | 100 | 0.02 | -
MTRQ | 1.24 | 25 | 0.31 | 2 X Rod / 1 X Air-coil
RWA | 8.33 | 50 | 4.17 | 3 axis
GPS Rx | 1.11 | 100 | 1.11 | L1
GPS Antenna | 0.11 | 100 | 0.11 | L1
EPS | 0.44 | 100 | 0.44 | PCDU / BCR
Battery | 0.89 | 0 | 0.00 | 40 Wh / Active Heater
UHF TRX | 3.33 | 10 | 0.33 | Beacon / Uplink
UHF Antenna | 0.04 | 100 | 0.04 | Deployable
S-band TRX | 2.11 | 3 | 0.06 | RX Only
S-band Antenna | 13.33 | 3 | 0.06 | Patch
Solar Array 1 | Generate | - | -8.84 | Deployable
Solar Array 2 | Generate | - | -0.50 | Body-mount
Power Margin |  |  | -1.31 | +14.0%

## Slide 20: Power Budget [4/4]
Emergency: Sun-pointing for Charging (Safe-hold)
  Beacon: 1 sec transmission by 30 sec / PCM eff. 90%
Subsystem H/W | P Consumption (W) | Duty Cycle (%) | P Operation (W) | Note
Imager | 3.00 | 0 | 0.00 | Multi-spectral
OBC 1 | 2.56 | 0 | 0.00 | SDR / FPGA
OBC 2 | 0.89 | 100 | 0.89 | Main / ADCS
FSS | 0.02 | 100 | 0.02 | -
MTRQ | 1.24 | 25 | 0.31 | 2 X Rod / 1 X Air-coil
RWA | 8.33 | 25 | 2.08 | 3 axis
GPS Rx | 1.11 | 0 | 0.00 | L1
GPS Antenna | 0.11 | 0 | 0.00 | L1
EPS | 0.44 | 100 | 0.44 | PCDU / BCR
Battery | 0.89 | 0 | 0.00 | 40 Wh / Active Heater
UHF TRX | 3.33 | 3 | 0.10 | Beacon / Uplink
UHF Antenna | 0.04 | 100 | 0.04 | Deployable
S-band TRX | 2.11 | 0 | 0.00 | Only RX Active
S-band Antenna | 13.33 | 0 | 0.00 | off
Solar Array 1 | Generate | - | -17.70 | Deployable
Solar Array 2 | Generate | - | -1.01 | Body-mount
Power Margin |  |  | -14.82 | +79.2%

## Slide 21: Power Generation (Simple)
#1. Rule of Thumb
  Pmax = Vmp X Imp X # of cells (or Voc X Vsc X solar cell efficiency)
  Paverage [W] = Pmax X 0.6
#2. Simple Mathematical Equation (Model) with Orbit and Attitude Dynamics
  Paverage [W] = solar irradiation [W/m2] X solar cell efficiency X total solar cell area [m2] X (1-cos(incidence angle, θ))
    Solar irradiation: (nominal) 1367 W/m2 (1326~1408 W/m2)
θ

## Slide 22: Power Analysis II: Advanced

## Slide 23: Overview: Energy Balance Analysis
Current Dynamics Modeling
  Li-polymer battery modeling (Clyde Space 3G EPS and battery)
  PV cell array modeling (Triple Junction AZUR solar cell)
Energy Balancing Simulation
  Battery SoC changes by power generation and consumption
    To analyze battery DoD over mission life
    Should have positive power budget in Normal mode
    To analyze the entrance criteria of safe mode
  Considered MPPT efficiency changes by body spin (D. M. Erb et al., 2011)
    MPPT in BCR with constant current charging method (fractional open circuit voltage/current)
  Considered PCM output efficiency by current

## Slide 24: Overview: Energy Balance Analysis
Simulation Architecture
Spacecraft
Orbit / Attitude
Dynamics
Power Generation
H/W Operations
PV Cell Model
Incidence Angle
Beta Angle
Eclipse
Battery Model
H/W Duty-cycled Operations
Power Consumption
State of Charge

## Slide 25: Li-polymer Battery Model [1/2]
Clyde Space Battery Model (Gao et al., 2002)
  Current dynamics of Li-polymer battery
    String of battery cells
    Power consumption considering duty cycle
    Power generation considering PV model
* Draft by KSML
[Power consumption example]

## Slide 26: Li-polymer Battery Model [2/2]
Model Feasibility
  Checked voltage draw by H/W operation
  Checked end-of-charge mode
[End-of-charge mode example]

## Slide 27: Photovoltaic Arrays IV-curve [1/2]
PV Array Modeling
  Current dynamics (Villalva, Gazoli, and Filho, 2009)
  * , : thermal voltage
  MATLAB function
    Input: (1) voltage, (2) irradiation (*tilted), (3) temperature
    Output: (1) current
    Parameter
      Rs = 7.95E-02 (Ohm, Equivalent Series Resistance)
      Rp = 2.62E+03 (Ohm, Equivalent Parallel Resistance)
      Alpha = 3.72 (Diode Ideality Constant)

## Slide 28: Photovoltaic Arrays IV-curve [2/2]
Perturbations on PV Cell
  (1) Temperature / (2) Irradiation (@TC = 28℃) effect on PV Cell
(1)
(2)

## Slide 29: AZUR Cell IV-curve [1/2]
2 Series PV Cells
  Maximum power point: 2.3902 W ( 2.4216 W)  98% of datasheet

## Slide 30: AZUR Cell IV-curve [2/2]
2 Series & 2 Parallel PV Cells
  Maximum power point: ~2707.86 mW < “max. P1 + max. P2” (~97%)
    Assumed a tilted orientation by 10 deg with respect to Sun vector
max. P1
max. P2

## Slide 31: Power Generation
Orbit and Attitude Dynamics
  Duration of day-side and eclipse + Beta angle (orbital parameters)
  Panel’s incidence angle w.r.t. Sun (attitude pointing accuracy)
Thermal, Radiative Effect + Man-made Degradation
[AZUR cell efficiency change by temperature of each cell ]

## Slide 32: Power Generation
Efficiency of Charge Method
  Maximum Power Point Tracker
  Battery Charge Regulator
  Albedo (10~20% of I⊙) as Margin
Inbuild MPPT on BCR
 only affected by tumbling
Need normal attitude operation strategy to maximize power generation
* Erb, Eaniel Martin, “Evaluating The Effectiveness of Peak Power Tracking Technologies for Solar Arrays on Small Spacecraft” (2011) University of Master’s Thesis.
Fractional Open Circuit Voltage

## Slide 33: Power Generation
Sun-pointing (Day-side)
  Safe-hold mode (for charging battery)
Nadir-pointing (Eclipse)
  Normal / Communication / Mission mode + *protect imager
<Pointing maneuver operations>
left: Sun-pointing, right: Nadir-pointing
Notes: nSight-1 (SCS) / Kepler (CS)

## Slide 34: Power Generation
Nadir-pointing
    Local Time on Ascending Node (LTAN), 13:30:00.000
    Sun-synchronous orbit, 500 km, Inclination 97.4 deg
    Beta angle, 32.94 deg
    * Maximum power point tracking / BUCK or SEPIC BCR efficiency

## Slide 35: Power Analysis III: Case Study

## Slide 36: Concept of Operations
H/W Operations: LEOP
Subsystem | Mode | Initialization | Deployment | Detumbling
 | Power (W) | Operation: on/off (duty) |  | 
Imager | 2.70 | Off | Off | Off
OBC1 | 0.60 | On | On | On
OBC2 | 2.30 | On | On | On
FSS | 0.02 | On | On | On
MTQR | 1.19 | Off | Off | 50% Usage
RWA | Speed: 0.90 / Torque: 7.50 | Off | Off | Off
GPS RX + ANT | 1.05 | Off | Off | Off
EPS | 0.40 | On | On | On
Battery (Heater) | 0.10 (Heater: 0.80) | On (Off) | On (Off) | On (Off)
S-band TRX (ANT) | TX: 1.83 / RX: 1.58 (TX: 10.70) | RX | RX | RX
UHF TRX (ANT) | 2.81 (TRX: 0.04) | TX: 1 sec / 30 sec | On (Knife: 2 W) | TX: 1 sec / 30 sec
Power Consumption (W) |  | 2.00 | 2.37 | 2.67
Peak Power (W) |  | 5.09 | 7.31 | 6.41
Generated Power (W) |  | TBA | TBA | TBA

## Slide 37: Concept of Operations
H/W Operations: Normal / Mission
Subsystem | Mode | Normal | SA Deployment | Mission
 | Power (W) | Operation: on/off (duty) |  | 
Imager | 2.70 | Off | Off | On (480 sec)
OBC1 | 0.60 | On | On | On
OBC2 | 2.30 | On | On | On
FSS | 0.02 | On | On | On
MTQR | 1.19 | 25% Usage | 25% Usage | 50% Usage
RWA | Speed: 0.90 / Torque: 7.50 | On / 25% Usage | On / 25% Usage | On / 50% Usage
GPS RX + ANT | 1.05 | Off | Off | Off
EPS | 0.40 | On | On (Knife: 2 W) | On (Knife: 2 W)
Battery (Heater) | 0.10 (Heater: 0.80) | On (Off) | On (Off) | On (Off)
S-band TRX (ANT) | TX: 1.83 / RX: 1.58 (TX: 10.70) | RX | RX | RX
UHF TRX (ANT) | 2.81 (TRX: 0.04) | TX: 1 sec / 30 sec | TX: 1 sec / 30 sec | TX: 240 sec
Power Consumption (W) |  | 6.58 | 6.95 | 10.49
Peak Power (W) |  | 7.57 | 18.91 | 25.78
Generated Power (W) |  | 8.91 | 8.91 | 8.91

## Slide 38: Concept of Operations
H/W Operations: Communication / Safe
Subsystem | Mode | Communication | Charge | Detumbling
 | Power (W) | Operation: on/off (duty) |  | 
Imager | 2.70 | Off | Off | Off
OBC1 | 0.60 | On | On | On
OBC2 | 2.30 | On | On | On
FSS | 0.02 | On | On | On
MTQR | 1.19 | Off | 25% Usage | 50% Usage
RWA | Speed: 0.90 / Torque: 7.50 | Off | Off | Off
GPS RX + ANT | 1.05 | Off | Off | Off
EPS | 0.40 | On | On | On
Battery (Heater) | 0.10 (Heater: 0.80) | On (Off) | On (Off) | On (Off)
S-band TRX (ANT) | TX: 1.83 / RX: 1.58 (TX: 10.70) | TX: 120 sec | RX | RX
UHF TRX (ANT) | 2.81 (TRX: 0.04) | TX: 240 sec | TX: 1 sec / 30 sec | TX: 1 sec / 30 sec
Power Consumption (W) |  | 7.14 | 2.33 | 2.67
Peak Power (W) |  | 35.81 | 6.41 | 6.41
Generated Power (W) |  | 8.91 | 18.00 | 18.00

## Slide 39: Energy Balance [1/5]
State of Charge Analysis
  Nadir-pointing in Normal mode (MPPT eff. ~95%): DOD ~ 11.1%
min 78.1%
end 86.8%
End of Charge, 8.26V

## Slide 40: Energy Balance [2/5]
State of Charge Analysis
  Attitude control in Mission mode (MPPT eff. ~80%): DOD ~ 17.4%
min 69.2%
end 76.9%
Payload Operation
UHF Communication

## Slide 41: Energy Balance [3/5]
State of Charge Analysis
  Communication mode in Eclipse (MPPT eff. ~95%): DOD ~ 14.8%
min 74.4%
end 83.1%
S-band Communication

## Slide 42: Energy Balance [4/5]
State of Charge Analysis
  Sun-pointing in Safe-Hold (MPPT eff. ~95%): DOD ~ 14.8%
min 50.0%
end 80.6%
MTQ / RWA for Sun-pointing

## Slide 43: Energy Balance [5/5]
State of Charge Analysis
  End-of-Charge (EoC) at 8.26 V
End of Charge, 8.26V

## Slide 44: Conclusion

## Slide 45: Summary
EPS Configuration
  Role in spacecraft, components, architecture, interface
EPS Analysis
  Power budget management
  EPS mathematical model design
  Energy balance analysis: integrated electrical power simulation
Key Words
  PCDU – PCM / PDM
  BCR – BUCK / SEPIC
  MPPT
  Energy Balance – DoD / SoC

## Slide 46
Thank You for Your Attention
Question & Answer